G-4500-3GWA G-4500D-3GWA G-4500P-3GWA G-4500PD-3GWA CPU 80 MHz internal microprocessor SRAM/Flash 512K/512K , real time clock, watchdog timer NVRAM 31 bytes, battery backup, data valid up to 10 years EEPROM 16 KB, retention > 40 years. 1,000,000 erase/write cycles Comm. Interface COM ports COM1:5-wire RS-232; COM2: RS-485; COM3:3-wire RS-232 Ethernet 10/100 Base-TX Ethernet controller 3G Interface Frequency Band Tri-band 2100/1900/850 MHz Data Transmission UMTS / HSDPA / HSUPA Downlink transfer: Max. 7.2Mbps; Uplink transfer: Max 5.76Mbps GSM Interface Frequency Band Quad-band 850/900/1800/1900 MHz GPRS connectivity GPRS class 12/10; GPRS station class B DATA GPRS Downlink transfer: Max. 85.6 kbps; Uplink transfer: Max 42.8kbps SMS SMS MT, MO, CB, Text and PDU mode SMS storage SIM card GPS Interface Support Channels - 32 Sensitivity - Tracking = up to -159 dBm (with external LNA) Cold start = up to -146 dBm (with external LNA) Acquisition Time - Hot start (Open Sky) = 2 s(typical) Cold start (Open Sky) = 36 s(typical) Protocol Support - NMEA 0183 version 3.01 LCD Interface General Effective display area - 80.61 mm x 14.37 mm (W x H) - 80.61 mm x 14.37 mm (W x H) Module Dimension - 93 mm x 70 mm x 1.6 mm (W x H x T) - 93 mm x 70 mm x 1.6 mm (W x H x T) Life Time - Expected life is more than 100,000 hours under normal operation - Expected life is more than 100,000 hours under normal operation Digital Output Output Channel 3 Output Type Open Collector (Sink/NPN) Load Voltage +30 VDC max. Load Current 100 mA max. Isolated Voltage Non-isolated Digital Input Input Channel 3 Input Type Source(Dry Type), Common Ground Off Voltage Level +1 V max. On Voltage Level +3.5 ~ +30 V Isolated Voltage Non-isolated Analog Input Input Channel 8 Resolution 12 - bit Input Range/Type 0 ~ 20 mA Sample Rate 1 KHz max. (Read one channel) Power Protection Power reverse polarity protection Frame Ground Protection ESD, Surge, EFT, Hi-Pot Power Requirement 15W; Unregulated +10 VDC ~ +30 VDC Power Consumption Idle: 75 mA @ 24 VDC; Data Link: 150 ~ 400 mA (peak) @ 24 VDC LED Indicators System Red 3G/GSM Yellow GPS Green Yes Mechanical Casing Metal Dimensions 47 mm x 142 mm x 168 mm (W x L x H) Installation DIN-Rall and wall mount Environment Operating Temperature -20 ~ +70 °C -15 ~ +55 °C -20 ~ +70 °C -15 ~ +55 °C Storage Temperature -40 ~ +80 °C -20 ~ +70 °C -40 ~ +80 °C -20 ~ +70 °C Humidity 5~90% RH, non-condensing

back

G-4500-3GWA CR Tri-band 3G WCDMA M2M Mini-Programmable Automation Controller (RoHS) G-4500D-3GWA CR Tri-band 3G WCDMA M2M Mini-Programmable Automation Controller with LCD display (RoHS) G-4500P-3GWA CR Tri-band 3G WCDMA M2M Mini-Programmable Automation Controller with GPS function (RoHS) G-4500PD-3GWA CR Tri-band 3G WCDMA M2M Mini-Programmable Automation Controller with LCD display and GPS function (RoHS)