| Hardware Specifications |
| --- |
| • Computer |
| CPU | V2201-E1 Series: Intel® Atom™ Processor E3815 (Single Core, 512K Cache, 1.46 GHz) V2201-E2 Series: Intel® Atom™ Processor E3826 (Dual Core, 1M Cache, 1.46 GHz) V2201-E4 Series: Intel® Atom™ Processor E3845 (Quad Core, 1M Cache, 1.91 GHz) |
| OS | Windows Embedded Standard 7 64-bit or Linux Debian 7 64-bit |
| System Memory | 1 DDR3 SO-DIMM slot, 8 GB max.• E3815 and E3826 support DDR3L-1066 • E3845 supports DDR3L-1333 |
| USB | 1 bootable USB 3.0 port, 2 bootable USB 2.0 ports (type A) |
| • Storage |
| mSATA | 1 internal mini-PCIe socket for OS storage |
| SD | 1 SD 3.0 (SDHC/SDXC) socket for storage expansion* |
|  | *W7E only supports SD 2.0 |
| • Audio |
| Output | Line-out interface (together with HDMI) |
| • Other Peripherals |
| Expansion Slot | 2 Mini-PCIe sockets• 1 USB signal, for Sierra Wireless 3G/LTE module • 1 USB + PCIe signal |
| μSIM | 1 μSIM slot |
| • Display |
| Graphics Controller | Intel® HD (integrated) |
| Connector Type | 1 HDMI connector (type A) |
| Display Interface | Supports HDMI 1.4a, 1920 x 1080 pixels @ 60/24 bpp |
| • Ethernet Interface |
| LAN | Auto-sensing 10/100/1000 Mbps ports (RJ45) x 2 |
| Isolation Protection | 1.5 kV |
| • Wireless SMA Interface |
| Wi-Fi | 2 SMA connectors |
| 3G/LTE | 2 SMA connectors |
| GPS | 1 SMA connector |
| • Serial Interface |
| Serial Standards | RS-232/422/485 software selectable ports (DB9 male) x 2 |
| • Serial Communication Parameters |
| Data Bits | 5, 6, 7, 8 |
| Stop Bits | 1, 1.5, 2 |
| Parity | None, Even, Odd, Space, Mark |
| Flow Control | RTS/CTS, XON/XOFF |
| Baudrate | 50 bps to 115.2 kbps |
| • Serial Signals |
| RS-232 | TxD, RxD, DTR, DSR, RTS, CTS, DCD, GND |
| RS-422 | TxD+, TxD-, RxD+, RxD-, GND |
| RS-485-4w | TxD+, TxD-, RxD+, RxD-, GND |
| RS-485-2w | Data+, Data-, GND |
| • Digital Input |
| Input Channels | DI x 4, source type |
| Input Voltage | 0 to 30 VDC at 25 Hz |
| Digital Input Levels for Dry Contacts | Logic level 0: Close to GND Logic level 1: Open |
| Digital Input Levels for Wet Contacts | Logic level 1: +3 V max Logic level 0: +10 V to +30 V (Source to DI) |
| Connector Type | 10-pin screw-fastened Euroblock terminal |
| Isolation | 3 kV optical isolation |
| • Digital Output |
| Output Channels | DO x 4, sink type |
| Output Current | Max. 200 mA per channel |
| On-state Voltage | 24 VDC nominal, open collector to 30 VDC |
| Connector Type | 10-pin screw-fastened Euroblock terminal |
| Isolation | 3 kV optical isolation |
| • LEDs |
| System | Power, user-defined |
| Storage | mSATA, SD |
| LAN | 2 LEDs per port (100/1000 Mbps) |
| Serial | 2 LEDs per port (Tx and Rx) |
| Wireless | Mini-PCIe 1, Mini-PCIe 2 |
| • Switches and Buttons |
| Power Switch | on/off (left-side panel) |
| Reset Button | For warm reboot (left-side panel) |
| • Physical Characteristics |
| Housing | Aluminum |
| Weight | 940 g |
| Dimensions | Without ears: 150 x 48.8 x 120.2 mm (5.91 x 1.92 x 4.73 in) With ears: 178 x 52.5 x 120.2 mm (7.01 x 2.07 x 4.73 in) |
| Mounting | DIN rail, wallmount |
| • Environmental Limits |
| Operating Temperature | • E1/E2 models: -40 to 85°C (-40 to 185°F) • E4 models: -40 to 70°C (-40 to 158°F) • E1-W/E2-W/E4-W models with Moxa recommended wireless modules (3G/LTE + Wi-Fi) installed: -40 to 70°C (-40 to 158°F) |
| Storage Temperature | -40 to 85°C (-40 to 185°F) |
| Ambient Relative Humidity | 5 to 95% (non-condensing) |
| Anti-Vibration | 5 Grms, 5 Hz to 500 Hz, 1 hr/axis w/ mSATA, SD |
| Anti-Shock | 100 g/11ms ±X, ±Y, ±Z, 3 shocks each axis w/ mSATA, SD |
| • Power Requirements |
| Input Voltage | 9 to 36 VDC (3-pin terminal block for V+, V-, SG) |
| Power Consumption | 18 W (2 A @ 9 VDC) |
| • Standards and Certifications |
| Safety | UL 60950-1, CSA C22.2 No. 60950-1-03 (60950-1-07), EN 60950-1, CCC, UL 508 |
| EMC | EN 55022 Class A, EN 61000-3-2 Class D, EN 61000-3-3, EN 55024, FCC Part 15 Subpart B Class A, EN 61000-6-2*, EN 61000-6-4* |
| Green Product | RoHS, CRoHS, WEEE |
|  | *Passed with AC/DC adapter. |
| • Reliability |
| Automatic Reboot Trigger | Software-programmable watchdog timer configurable from 1 to 255 seconds |
| • Warranty |
| Warranty Period | 3 years |
| Details | See www.moxa.com/warranty |
|  | Note: These hardware specifications describe the embedded computer unit itself, but not its official accessories. In particular, the wide temperature specification does not apply to accessories such as power adapters and cables. |
| Software Specifications |
| • Linux |
| OS | Linux Debian 7 |
| Web Server (Apache) | Allows you to create and manage web sites; supports PHP and XML |
| Terminal Server (SSH) | Provides secure encrypted communications between two un-trusted hosts over an insecure network |
| File System | EXT 4 |
| Internet Protocol Suite | TCP, UDP, IPv4, SNMPv1/v2c/v3, ICMP, ARP, HTTP, SSH 1.0/2.0, SSL, DHCP, NTP, NFS, Telnet, FTP, TFTP, PPP, PPPoE |
| Internet Security | OpenVPN, iptables firewall |
| Secure Shell for Remote Access | SSH allows remote logins to a secure encrypted console from any connected network |
| Dial-up Networking | PPP Daemon for Linux that allows Unix machines to connect to the Internet through dialup lines, using the Point-to-Point Protocol (PPP). Works with ‘chat’, ‘dip’, and ‘dialu dip’, and ‘diald’, among (many) others. Supports IP, TCP, UDP |
| File Server | Enables remote clients to access files and other resources over the network |
| Watchdog | A watchdog timer that triggers a system reset upon software freezes, for both specific applications and system-wide failures. |
| Application Development Software | • Moxa API Library • GNU C library • Perl |
| Embedded Self-Health Maintenance Software | Moxa Proactive Monitoring |
| • Windows Embedded Standard 7 |
| Core OS | • 64-bit support • Remote Client • Remote Procedure Call |
| Applications and Services Development | • Remote Desktop Protocol 7.1 • COM OLE Application Support • COM+ Application Support • MSMQ |
| Internet Services | • Internet Explorer 8.0 • IIS 7.0 |
| Diagnostics | • Common Diagnostic Tools • Problem Reports and Solutions |
| Fonts | Western, Middle Eastern, South East Asian, and South Asian FontsRailway Computers 4 www.moxa.com |
| Graphics and Multimedia | • MPEG Layer-3 Audio Codecs (MP3) • MPEG4 Decoders • DirectX and Windows Device Experience |
| Management | • Group Policy Management • Windows Management Instrument (WMI) • Windows Update |
| Networking | • Extensible Authentication Protocol (EAP) • Internet Authentication Service • Telnet Server • Bluetooth • Domain Services • Network Access Protection • Network and Sharing Center • Quality of Service • Remote Access Service (RAS) • Telephony A |
| Security | • Credential Roaming Service • Credentials and Certificate Management • Windows Authorization Manager (AZMAN) • Windows Security Center • Active Directory Rights Management • Security Base • Encrypted File System (EFS) |
| Embedded Features | • Enhanced Write Filter (EWF) • File-Based Write Filter (FBWF) • Registry Filter • WSDAPI for .NET |
| File Systems and Data Store | • Windows Data Access Components • Windows Backup and Restore |
| Maintenance | Moxa Proactive Monitoring & Moxa Smart Recovery |